Internet Monitor /
Modem Power Switcher
I'm on VirginMedia Cable. So, I want to watch some of the 'Linux Action Show' over breakfast but the Internet has gone off again. So now I have to mess about switching the modem off/on and waiting, hopefully, for a connection.
This project aims to circumvent this problem.

---
Methodology
Make this an additional job for my RasPi server.
Set up a cron* job to run at 15 minute intervals.
1. Cron job triggers a program which pings a web site.
2. If there is no response from the web site modem is switched off for 5 minutes.
3. Goto 1
*The name cron comes from the Greek word for time, χρόνος chronos.

---
START
Wait for Cron Trigger
ping virginmedia.com
Wait 5 minutes
OK?
Set GPIO pin to '0'
Y
N
ping bbc.co.uk
OK?
Y
N
Set GPIO pin to '1'

---
How the ping result is picked up
Part of a function:
function pingURL($url,$pingfile)
{
exec("ping -c1 ".$url." > ".$pingfile);
….......
….....
}

---
PHP Program
Configuration
$pingfile="/home/pi/pingfile.txt";
$logfile="/home/pi/netmonitor.log";
$url1="virginmedia.com";
$url2="bbc.co.uk";
$time=300;//time relay is latched (modem off) in seconds

---
The Switching of the Modem
The Raspberry Pi has GPIO (General Purpose Input Output) pins. These can be used to connect hardware inputs/outputs.
In our case we are going to connect a transistor which drives a relay (an electro-mechanical switch).
The relay: Rather than switching the mains supply to the modem, switches, instead, the modem's low voltage power supply.
Transistor
RasPi GPIO pin
Modem
Relay
Power
Supply
Mains

---
Controlling the GPIO pins
Several ways of doing this.
Easiest I found was to make use of a ready built
open source program*
*Courtesy of Gordon Henderson
http://tinyurl.com/1234GPIO

---
How to install the GPIO program
On the web site choose the latest version, then choose 'snapshot'.
Once downloaded to the Pi do this:-
tar xfz wiringPi-xxxxx.gz
cd wiringPi-xxxxxxx
./build

---
PHP Program
GPIO function
function setRelayOn($time)
{
        exec ( "gpio -g mode 17 out");
        exec ( "gpio -g write 17 1");
        exec ( "gpio -g read 17",$status);
        print_r ($status);
        sleep($time);
        exec ( "gpio -g write 17 0");
        exec ( "gpio -g read 17",$status);
        print_r ($status);
}